## Slide 1: Environmental Risk Management Action Plan A Practical Framework for Baltic Marina Managers Interreg South Baltic Program 2021-2027
NAME OF PREZENTER
Place and DATE
Based on the Environmental Risk action management plan..

## Slide 2
What This Session Is About
A practical, science-based tool for every Baltic marina
This session introduces the Environmental Risk Management Action Plan (ERMAP) — a structured framework developed within the ECOMARINAS project to help marina managers:
1
Identify and assess the environmental risks in their marina
2
Implement practical, proportionate control measures
3
Meet legal obligations under MARPOL, HELCOM and EU directives
4
Build a continuous improvement culture — not just a compliance checklist
💡 The ERMAP follows ISO 14001:2015 principles — systematic identification, risk assessment, control measures, and continuous improvement.

## Slide 3
Why Does It Matter? The Baltic Sea Context
97%
of Baltic Sea affected by eutrophication
Slow
water exchange — pollutants don't flush away
High
seasonal vessel density in enclosed basins
Low
natural self-purification
capacity
Marina as Hotspot
Even small marinas can affect aquatic ecosystems through nutrient loading, chemical contamination, habitat alteration, noise, light, and invasive species spread — particularly in the Baltic's enclosed conditions.
The Solution: ERMAP
Proactive environmental risk management improves regulatory compliance, social acceptance, and the long-term sustainability of marina operations — turning obligations into competitive advantage.

## Slide 4
The ERMAP: Six Risk Areas
Each area has its own risk matrix, control points, and good practice measures
1
Wastewater Management
• Risk matrix (likelihood × severity)
• Control measures & good practices
2
Hazardous Liquids
• Spill prevention & containment
• Emergency response procedures
3
Water Quality Protection
• Monitoring, baselines, reporting
• Biodegradable products, wash-down zones
4
Invasive Species Prevention
• Hull inspections & clean-drain-dry
• Biosecurity awareness & signage
5
Plastic Pollution
• Waste segregation & Seabins
• Microplastic monitoring
6
Additional Risks
(Fire, Noise, Light, EMS)
• Fire plans, quiet hours, EMS audits
• ISO 14001-aligned management

## Slide 5
How Environmental Risk is Assessed
Likelihood × Severity = Risk Rating (aligned with ISO 14001:2015)
Risk Rating = Likelihood (L) × Severity (S) | Scale: 1–25
LOW
Score: 1–5
Manage through routine procedures & monitoring
MEDIUM
Score: 6–11
Implement mitigation measures & periodic review
HIGH
Score: 12–19
Immediate operational controls & management supervision
EXTREME
Score: 20–25
Urgent corrective action; emergency planning required
Each risk area is evaluated using this matrix — results determine whether action is routine, urgent, or emergency-level.

## Slide 6
1. Wastewater Management
Indicator: Pump-out facilities, holding tanks, discharge prohibition signage
Key Sources of Risk
Activity / Source
L
S
Risk
Vessel blackwater discharge
4
5
HIGH
Vessel greywater discharge
3
4
MED–HIGH
Marina sanitary facilities
2
4
MEDIUM
Maintenance wash-down runoff
3
4
MED–HIGH
Pump-out system failure
2
5
MED–HIGH
Good Practice Measures
✓ Install accessible pump-out stations — maintain logs monthly
✓ Mandatory certified holding tanks on all vessels
✓ Connect sanitary facilities to municipal wastewater treatment
✓ Post multilingual 'No Discharge' signs at all berths
✓ Emergency response plan for pump-out system failures
✓ Monitor dissolved oxygen, BOD, and fecal indicator bacteria

## Slide 7
2. Hazardous Liquids Management
Indicator: Spill kits, secondary containment, trained staff, written procedures
⚠ Survey finding: 56% of South Baltic marinas have NO systems to prevent hazardous liquid spills — the most common reason given was 'Not Necessary'
Activity
L
S
Risk
Key Control
Fuel transfer to vessels
4
5
HIGH
Controlled fueling, drip trays, trained staff
Fuel storage tanks
2
5
MED–HIGH
Secondary containment, regular inspections
Oil & lubricant handling
3
4
MED–HIGH
Bunded storage, spill kits
Chemical & solvent use
3
4
MED–HIGH
Proper labelling, limited on-site quantities
Maintenance area runoff
3
4
MED–HIGH
Designated work areas, containment bunds
If it's not visible, stocked and staff-trained — it does not exist. A spill kit at the dock is the minimum.

## Slide 8
3. Water Quality Protection
Indicator: Monitoring data, containment zones, maintenance area controls
Risk Assessment
Activity
L
S
Risk
Surface runoff from docks
4
3
HIGH
Vessel maneuvering / prop wash
3
3
MEDIUM
Fuel handling & minor spills
3
4
HIGH
In-water hull cleaning
4
4
HIGH
Uncontrolled wash-down
3
3
MEDIUM
Key Monitoring Indicators
📊 Nutrients: Total nitrogen and phosphorus
📊 Turbidity / total suspended solids
📊 Dissolved oxygen levels
📊 Petroleum hydrocarbon indicators
📊 Fecal indicator bacteria (after sewage incidents)
📊 Sediment monitoring for long-term contamination
Good practice: Monitor seasonally, log results, share with authorities in annual report.

## Slide 9
4. Invasive Species Prevention
Indicator: Hull inspection protocols, clean-drain-dry signage, biosecurity records
⚠ 37% of South Baltic marina managers believe invasive species prevention measures are 'Not Necessary' — despite hull fouling being the #1 vector
Hull Fouling
Biofouling on recreational vessels transports invasive species between marinas. Most common & highest-risk pathway.
L:4 × S:4 = HIGH
Equipment Transfer
Anchors, ropes, fenders and diving gear moved between water bodies without cleaning.
L:4 × S:4 = HIGH
Residual Bilge Water
Larvae and microorganisms in bilge, live wells and ballast compartments.
L:3 × S:3 = MEDIUM
Marina Structures
Submerged pontoons and moorings provide habitat for invasive colony establishment.
L:3 × S:3 = MEDIUM
Clean • Drain • Dry Inspect hull at check-in • Post biosecurity signage • Log incidents • Coordinate with national biosecurity authorities

## Slide 10
5. Plastic Pollution Management
Indicator: Waste segregation infrastructure, Seabin deployment, cleanup records
Risk Matrix
Source
L
S
Risk
Improper vessel waste disposal
4
3
HIGH
Visitor littering
4
4
HIGH
Marina maintenance debris
3
3
MEDIUM
Boat cleaning / hull abrasion
3
4
HIGH
Synthetic rope & fender wear
2
3
MEDIUM
Practical Solutions
♻ Segregated waste stations with recycling fractions on pontoons
♻ Seabins / PortBins for surface debris and microplastics
♻ Ban single-use plastics at marina café and shop
♻ Shrink wrap take-back programme for boat owners
♻ Quarterly marina seabed and dock clean-up events
♻ Log waste quantities by type — identify key sources
Lithuania: 71% of marinas have no plastic reduction measures · Germany: 73% do · Sweden: 86% do

## Slide 11
6. Additional Environmental Risks
Fire, noise, light pollution, electromagnetic disturbance, and EMS management gaps
Fire Risk
HIGH (L3×S4)
Toxic gases & contaminated firefighting runoff.
Fire prevention systems, emergency plans, joint drills with fire brigade.
Noise Pollution
MEDIUM (L3×S3)
Engine, generator & maintenance noise disrupts fish behaviour and marine mammals.
Quiet-hour policies, low-noise equipment maintenance.
Light Pollution
MEDIUM (L3×S3)
Artificial lighting disrupts fish, sea birds and invertebrate circadian rhythms.
Shielded, directional, low-intensity lighting with timers.
EMS Management Deficiencies
MED–HIGH (L3×S4)
Unclear policies, poor staff training, lack of coordination. Increases incident probability.
ISO 14001-aligned EMS, audits, certification (Blue Flag, ECOMARINAS).
Electromagnetic Disturbance
Shore power cables generate EMFs affecting electrosensitive species.
Best-practice cable installation and placement.
LOW–MED (L2×S3)

## Slide 12
What Good Practice Looks Like
Before & After — applying the ERMAP in your marina
✗ Before ERMAP
✓ After ERMAP
✗ No written spill response procedure at fuel dock
✓ Laminated spill response card posted + spill kit stocked
✗ Hazardous waste mixed with household bins
✓ Locked, labelled hazardous waste storage, separate contractor
✗ No hull inspection at vessel check-in
✓ 'Check-in hull protocol' form completed for arriving vessels
✗ No water quality baseline data available
✓ Seasonal monitoring log: O₂, turbidity, nutrients on file
✗ Pump-out out of service — no maintenance log
✓ Monthly pump-out service log; boaters informed at check-in
Document before/after with photos — visible change is the most powerful evidence for your board and for inspectors.

## Slide 13
Policy & Legal Framework
The ERMAP aligns with all key international, regional and EU obligations
International
• MARPOL Convention — pollution from ships (sewage, garbage, oil, hazardous substances)
• HELCOM (Helsinki Convention) — nutrient reduction, waste management, invasive species in the Baltic
EU Directives
• Water Framework Directive (2000/60/EC) — good ecological & chemical status of surface waters
• Marine Strategy Framework Directive (2008/56/EC) — good environmental status of marine waters
• Invasive Alien Species Regulation (EU) 1143/2014 — prevention and management of invasive species
Voluntary Frameworks
• ISO 14001:2015 — Environmental Management System framework underpinning the ERMAP
• Blue Flag for Marinas — wastewater, waste, energy, biodiversity, and awareness criteria
• ECOMARINAS Certification — integrating ERMAP outcomes into the certification indicator system

## Slide 14
Implementation Roadmap
A phased approach to embedding ERMAP in your marina operations
Phase 1
0–30 days
Assess & Document
→ Complete the ERMAP risk matrices for all 6 areas
→ Identify your highest-risk activities (score 12–25)
→ Audit existing procedures & documentation gaps
Phase 2
30–90 days
Quick Wins
→ Post laminated spill response procedure at fuel dock
→ Label all waste bins; add hazardous waste lockbox
→ Train all staff on spill response & pump-out procedure
Phase 3
90 days–6 months
Structural Improvements
→ Upgrade pump-out accessibility; schedule maintenance
→ Install Seabin or PortBin in marina basin
→ Begin baseline water quality monitoring log
Phase 4
Ongoing
Monitor & Improve
→ Annual ERMAP review — update risk ratings
→ Pursue ECOMARINAS or Blue Flag certification
→ Document before/after improvements for board & inspectors
Within 90 days, every participating marina should implement at least one visible improvement — documented with before/after evidence.

## Slide 15
Roles & Responsibilities
Effective ERMAP implementation requires clear ownership at every level
Marina Manager / Owner
ERMAP oversight, annual review, investment decisions, certification pursuit
Harbour Master / Operations
Day-to-day compliance, staff briefings, incident reporting, monitoring logs
Marina Staff
Spill response, waste management, hull check-in protocol, visitor communication
Boat Owners & Visitors
Compliance with discharge rules, proper waste disposal, hull cleaning cooperation
Local Authorities
Permit issuance, inspection coordination, funding access, policy alignment

## Slide 16
Monitoring, Review & Continuous Improvement
The ERMAP is a living document — not a one-time checklist
1 — PLAN
Identify risks,
set targets & procedures
2 — DO
Implement controls,
train staff, act
3 — CHECK
Monitor, measure,
log incidents & data
4 — ACT
Review results,
correct & improve
ISO
14001
Annual ERMAP review · Update risk ratings based on monitoring data · Integrate with certification audit cycle

## Slide 17
ECO ⚓ MARINAS
Interactive Reflection
Which risk area is the biggest challenge in YOUR marina right now?
Wastewater &
Pump-out
Hazardous
Liquids
Water Quality
Monitoring
Invasive
Species
Plastic
Pollution
Fire / Noise /
EMS
Use Kahoot, show-of-hands, or open discussion

## Slide 18
20 minutes · Groups of 3–4 · Use the ERMAP template worksheet
Working in small groups, complete the following for your marina (or a marina you know):
Step 1
Pick your top 3 risks:
From the 6 ERMAP areas, identify the three activities with the highest environmental risk score in your marina. Rate each: Likelihood (1–5) × Severity (1–5).
Step 2
Identify your gaps:
For each high-risk item: what control measures are currently missing? What is the most important single document or procedure not yet in place?
Step 3
Build your 90-day action:
For each gap, define: What will you do? Who is responsible? What evidence will you produce (photo, log, signed procedure)? Deadline?
Outcome: Each group presents one commitment — a specific action they will take within 90 days, with measurable evidence.

## Slide 19
ERMAP & ECOMARINAS Certification
Every ERMAP action contributes directly to certification indicators
ERMAP Risk Area
ECOMARINAS Indicator
Certification Scheme
Wastewater Management
Wastewater & Sewage Management Indicator
Blue Flag, Clean Marina
Hazardous Liquids
Hazardous Substances Indicator
ISO 14001, Blue Flag
Water Quality
Water Quality Monitoring Indicator
ECOMARINAS, Blue Flag
Invasive Species
Biodiversity & Habitat Indicator
ECOMARINAS
Plastic Pollution
Waste Infrastructure & Sorting Indicator
Blue Flag, ECOMARINAS
Additional Risks (EMS)
Environmental Management System
ISO 14001:2015
💡 The ERMAP helps turn your invisible compliance work into visible, certifiable value — evidence for inspectors, owners, and boaters alike.

## Slide 20
From Compliance Cost to Competitive Advantage
Environmentally compliant marinas — with a documented ERMAP — are more attractive to:
International Cruising Yachts
Skippers from Germany, Scandinavia and UK actively research environmental credentials before selecting a marina destination.
Charter Operators & Clubs
Sustainability standards increasingly specified in facility agreements — ECOMARINAS certification is a qualifying signal.
Grant & Funding Bodies
EU and national programmes for marina infrastructure prefer or require environmental certification.
Tourism Authorities
Coastal tourism promotion increasingly uses marina eco-certification as a quality indicator for sustainable destinations.
The ECOMARINAS standard turns your invisible ERMAP compliance into visible, marketable value.

## Slide 21
Your Three Most Important Takeaways
1
Risk is manageable — if it is documented
Most penalties in Baltic marinas are for missing documentation, not active pollution events. A written procedure and a maintenance log are your most powerful compliance tools.
2
The ERMAP is proportionate
You do not need to solve everything at once. The risk matrix tells you where to start — High and Extreme risks first, Low risks through routine monitoring.
3
Behaviour change is the cheapest improvement
Laminated cards, check-in hull forms, boater signage — these cost almost nothing and are noticed immediately by inspectors, visitors, and certifiers.
Now let's look at how real Baltic marinas implemented these changes — and what you can apply immediately.

## Slide 22
Summary & Call to Action
ECOMARINAS is closing the gap between interest and action
🗂
Download the ERMAP
Request the full Environmental Risk Management Action Plan template from the ECOMARINAS project office.
📋
Complete your risk matrices
Use the 6 risk area worksheets. Score likelihood × severity for each activity at your marina.
📸
Document your starting point
Take before-photos of your current situation. This is your baseline for the 90-day improvement cycle.
🤝
Join the ECOMARINAS network
Share your action plan, connect with Baltic marina peers, and apply for ECOMARINAS certification.
🏆
Pursue certification
Blue Flag, ISO 14001, or ECOMARINAS — any certification turns compliance into competitive advantage.
📅
Gdansk Forum 2027
Join the Sustainable Sailing Infrastructure Forum — where Baltic marina managers share what works.

## Slide 23
Environmental Risk Management
Action Plan
Questions? Join the network. Make your marina great.